Quick Start Guide
Icecast-enabled Studio-to-Transmitter Link Encoder
# Basics and Cabling
Now that you've unpacked the box and torn into the goods, make sure everything is here:
1. Studio-to-transmitter link (STL) enclosure, “the appliance”
2. Power cable
3. Ethernet cable
4. These instructions
Place the STL in an appropriate place for your installation. We suggest a 19-inch rack, but put it anywhere safe and out of the way. It's not intended for use in a broadcast studio because the power supply fan is audible in quiet environments. Make sure you provide for a LAN connection (up to 1Gbps, [10000BaseT]).
You also need to supply two balanced audio cables (one each for the Left and Right channels, for a stereo broadcast) to the STL. Depending on the audio card model in your STL encoder, you need cables with either male ¼-inch TRS connectors or male XLR connectors to connect to the STL.
# Initial Network Configuration and Sign-in
The MAC address for this unit is:
Once you have a network cable connected to your LAN switch, plug the power cable in to the STL (it will turn on as soon as you plug in the power cable). It is configured to obtain an Internet Protocol (IP) address from your DHCP server. Using the above MAC address, you may want to configure your DHCP server to issue a statically assigned, or “static reservation” to the STL.
Alternatively, you can simply look up the IP address on the STL once it is running, and connected to the network. To do this, plug in a VGA or HDMI display and USB or PS/2 keyboard to the appropriate connectors on the rear of the STL. Log in as user 'pmwtech' with the password 'phantommachineworks'. Type the command ip addr and press Enter. Note the IP address associated with the interface named eth0.
# Streaming Client Configuration
The STL includes an Icecast streaming server. The server is configured with the following parameters. You will need to configure your client(s) to connect to the server.
Icecast server IP address: provided by your DHCP server (see above)
Icecast administrative credentials: username: kwvh-admin password: pMIqDUXu9HCzFhf2FWvl5%FZZ+mNsH0T
Icecast source client credentials: username: source password: hiQ8eCDbXyS0txD2GigSZ@3zShh7hD%x
Icecast source client connection details:
bind-address: 127.0.0.1, TCP port: 8080
Icecast streaming client connection details:
bind-address: 0.0.0.0, TCP port: 8000
Icecast log details:
Access log: /var/log/icecast2/access.log
Error log: /var/log/icecast2/error.log
# Advanced Configuration Details
### Audio Routing Configuration
The audio flow through the STL is shown in FIGURE.
# Document History

Revision Date	Editor	Change Summary
2015-11-20	David Klann	Initial revision