Quick Start Guide
Icecast-enabled Studio-to-Transmitter Link Encoder
# Basics and Cabling
Now that you've unpacked the box and torn into the goods, make sure everything is here:
1. Studio-to-transmitter link (STL) enclosure
2. Power cable
3. Ethernet cable
4. These instructions
Secure the STL in an appropriate place for your installation. We suggest a 19-inch rack, but put it anywhere safe and out of the way. It's not intended for use in a broadcast studio because the power supply fan is audible in quiet environments. Make sure you provide for a LAN connection (up to 1Gbps, [10000BaseT]).
You also need to supply two balanced audio cables (one each for the Left and Right channels for a stereo broadcast) to the STL. Depending on the audio card model in your STL encoder, you need cables with either male ¼-inch TRS connectors or male XLR connectors to connect to the STL.
# Cabling and Connections
1. Use the Ethernet cable provided (or your own) to connect the STL to your LAN switch.
2. Connect audio cables from your “upstream” device (distribution amplifier, EAS unit, audio switcher, etc.) to the Left and Right inputs of the STL.
3. Use the power cable provided to plug in your STL. It will turn on automatically.
# Network Configuration and Sign-in
The MAC address for this unit is:
You may be able to start using your STL as soon as you turn it on. It is configured to obtain an Internet Protocol (IP) address from your DHCP server. Using the above MAC address, you may want to configure your DHCP server to issue a statically assigned IP address, or “static reservation” to the STL.
You can look up the IP address on the STL once it is running, and connected to the network. You may need to do this if you have not assigned a static reservation for the STL in your DHCP server. To retrieve the IP address from the STL, plug in a VGA or HDMI display and USB or PS/2 keyboard to the appropriate connectors on the rear of the STL. Log in as user 'pmwuser' with the password 'pmwuser'. Use the menu to display networking configuration and various system service status. Note the IP address for configuring your Icecast streaming clients.
# Streaming Client Configuration
The STL includes an Icecast streaming server. The server is configured with the following parameters, which you will need to configure your client(s) (transmitter, stream monitor, etc.) to connect to the server.
Icecast server IP address: provided by your DHCP server (see above)
Icecast streaming client connection details:
stream URL: http://<STL-IP-ADDRESS>:8000/live
Icecast administrative credentials:
username: kwvh-admin
password: pMIqDUXu9HCzFhf2FWvl5%FZZ+mNsH0T
Icecast log details:
Access log: /var/log/icecast2/access.log
Error log: /var/log/icecast2/error.log
# Theory of Operation and Advanced Configuration
### Audio Routing Configuration
Audio flows through the Phantom Machine Works STL as shown in Figure 1.
### Analog Audio

Analog Audio
JACK
Audio Transport
Liquidsoap
Encoder
Icecast
Stream Server

Figure 1: Audio routing through the PMW STL
This is the source of the audio signal, mixed and routed to the audio card in the STL.
### JACK Audio Routing Service
The PMW STL uses the open source JACK (Jack Audio Connection Kit) application to route analog audio from the sound card to the digital encoder application. Think of JACK as a software patch panel you use to connect audio outputs to audio inputs. JACK is configured in its startup script /usr/local/bin/pmw-jackd-start.sh. The parameters in this script are configured to search for and route the audio from the PCIe audio card to the Liquidsoap encoder.
### Liquidsoap Encoder
Your STL uses the open source application Liquidsoap to convert analog audio signals into digital format. This conversion is known as “encoding”. Liquidsoap is configured in the plain text file /etc/liquidsoap/10-stl-encoder.liq. This script (written with the Liquidsoap scripting language) sets all the parameters for the ingestion of the analog audio and its conversion to digital format. On encoding the audio, liquidsoap then routes the digital audio to the Icecast stream server.
### Icecast Stream Server
Your customized STL uses the open source Icecast stream server to transport the station's digitized audio signal to the transmitter. Icecast is configured in the plain text file /etc/icecast2/icecast.xml to accept digital audio from its “source client” (Liquidsoap, in this case) and distribute that audio to the streaming clients. We expect that there will be few streaming clients: primarily the transmitter, and possibly a workstation in the studio configured to monitor the stream.
# Document History
Revision Date	Editor	Change Summary
2015-11-20	David Klann	Initial revision
2015-11-26	David Klann	Document editor suggested changes, cleanup